## Slide 1: The Nuclear Fuel Cycle
Mary Lou Dunzik-Gougar, PhD
ANS Teachers’ Workshop
2014

## Slide 3: Uranium Mining
Open pit (strip) mining
Underground mining
In situ leaching

## Slide 5: Uranium Milling
  Ore is crushed
  Uranium is separated
  U3O8 “yellow cake” produced

## Slide 7: Uranium Conversion (to UF6 gas)
Impurities removed
Uranium combined with fluorine
UF6 gas produced
  - Gaseous form facilitates
  enrichment
UF6 containers

## Slide 9: U Enrichment
Natural U is > 99% 238U and only ~ 0.7% 235U
Separation of 235UF6 and 238UF6 based on (very small) mass difference
UF6 enriched from 0.7% 235U to 3%-5% 235U
Diffusion
Centrifugation

## Slide 11: Fuel Fabrication
Uranium Oxide Ceramic Fuel Pellets
Enriched UF6 gas converted to uranium oxide (UO2) solid
Notes: Finally, the uranium hexafluoride is shipped to a fuel fabricator, where it is manufactured into solid ceramic pellets, about the size of the end of a finger.

## Slide 12: Fuel Fabrication
Fuel rods filled with ceramic pellets are
grouped into fuel assemblies

## Slide 13: Fuel Fabrication
A pressurized water reactor fuel assembly

## Slide 15: Reactors
Diablo Canyon nuclear power plant in the U.S.

## Slide 17: In the reactor, 235U fissions to produce . . .
Neutrons may
  Cause new fissions to occur
  Be absorbed to form unstable, radioactive nuclide
Neutrons
Energy
Fission Products
Neutron

## Slide 18: Fuel Consumption in the Reactor
Fuel is in reactor for 4 – 6 years
U consumed, fission products and transuranics (mostly Pu) produced
4%
3.5%
94%
235U
238U
Pu
Fission
Products
Transuranics
(or Actinides)
96%
Fresh Fuel
Used Fuel
Notes: I like to talk about this in a simple way as: things lighter than U <---> U <---> things heavier than U

## Slide 20: Used Nuclear Fuel Storage
Used fuel first stored in pool at least 5 years
  Cooling and shielding
Older fuel can move to dry casks
  Air cools
  Steel and concrete shields

## Slide 22: Fuel recycle/reprocessing
4%
3.5%
94%
235U
238U
Pu
Fission
Products
Transuranics
(or Actinides)
96%
Fresh Fuel
Used Fuel

## Slide 24: Geologic Repository
The choice of countries worldwide
U.S. has studied Yucca Mt., Nevada as potential location

## Slide 25: The End . . .