## Slide 1: Introduction to Nuclear Energy
Candace Davison
Senior Reactor Operator
Penn State University

## Slide 2: Energy in the United States
43%
24%
19%
11%
2%
Notes: Electricity generation over time in the United States.

## Slide 3: Energy in the United States
Notes: Q: It looks like energy use per capita has plateaued in the last ~30 years. Does that mean that we have no need for new energy production?
Q: What historical/economic events can you point out on this graph?
A: Among others: oil crisis and recession of late 1970s/early 1980s; Great Recession of late 2000s.

## Slide 4: How Much Electricity?
Chart: 
| Coal 39% | Natural gas 27% | Nuclear 19% | Hydropower 6% | Biomass | Geothermal | Solar | Wind | Petroleum | Other Gases
 | 39.1 | 27 | 19.1 | 6 | 1.7 | 0.4 | 0.4 | 4.4 | 1 | 0.9
Notes: This is for the US

## Slide 5: What is electricity?
Electricity is the flow of electrons.
Sometimes you see it in the sky in a lightning streak.
Sometimes you hear it crackle when you take off a sweater.
How is Electricity Made?
Notes: Ask students: Is electricity a primary or secondary source of energy? (Answer: Secondary) Is coal a primary or secondary source? (Answer: Primary)
Ask students: Have you ever had to do without electricity for a while? What did you have to stop doing?

## Slide 6: Generating Electricity
Burn fuel or
split atoms
Heat water to make steam
Steam turns turbine
Turbine turns generator
Electricity is generated!
Moving water or wind turns turbine
or
Notes: Pause here for students who are visual learners to draw their own picture notes. The drawing illustrates a turbine. As steam flows over the blades of the turbine, kinetic energy turns the shaft. A coil of wire attached to the shaft of the generator turns inside a magnet. This causes
electrons to flow in the coil – and the flow of these electrons creates electricity.
Define the word generate as “to produce”. Generate is a word often used in describing the production of electricity.

## Slide 7: Fusion vs. Fission
Fusion
Two hydrogens collide
Making Helium and energy
Average of 3.5 MeV per fusion
Fission
Uranium 233, 235, 238
Average of 207 MeV per fission
Notes: Use fusion and the sun to help tour understand the idea of fission and how they are different.
commons.wikimedia.org
giphy.com

## Slide 8: Energy From Fission
Energy from one Uranium Fuel Pellet can equal…
Notes: Expand on just how much energy fission can produce and why its useful. Use the comparisons on the slide for energy references.
geoinfo.nmt.edu
forum.nationstates.net
www.pv-magazine.com
www.101qs.com

## Slide 9: Energy From Fission
About 1 ton of coal
17,000 ft3 of natural gas
32 mi2 of Solar Panels or Wind Turbines
Notes: Expand on just how much energy fission can produce and why its useful. Use the comparisons on the slide for energy references.
geoinfo.nmt.edu
forum.nationstates.net
www.pv-magazine.com
www.101qs.com

## Slide 10: Fission
Nuclear Reactors harness fission for various reasons.
Producing clean electricity
Research
Notes: Explain the difference between Research Reactors and Power Generation Utilities and how they utilize fission.
safetyfirst.nei.org
www.cpepweb.org

## Slide 11: Nuclear Propulsion

## Slide 12: Nuclear Energy
Notes: Explain process of using a reactor to generate electricity.
galleryhip.com

## Slide 13: Fuel Assembly Designs

## Slide 14: Core Loadings

## Slide 15
Notes: Elaborate on fission process and chain reaction. Briefly discuss criticality.
physics.tutorvista.com

## Slide 16: Control Rods
Control Rods balance the fuel and allow the reactor to be started up and shut down.
Control Rod materials have a higher probability of neutron absorption than the fuel.
  Boron 5x higher
  Cadmium 30x higher
  Gadolinium 350x higher
  TRIGA had 4 control rods
  Power reactors have dozens of rods

## Slide 17: Nuclear Power Reactors
Nuclear power reactors are classified by their:
  Neutron energy
    Thermal, < 1 ev
    Fast, >150 keV
  Neutron moderator: H2O, D2O, graphite
  Coolant: H2O, D2O, gas (CO2, He), liquid metal (Na)

## Slide 18: Nuclear Power Reactors
LWR: Light water reactor
  BWR: Boiling water reactor
  PWR: Pressurized water reactor
  VVER: Russian PWR (Vodo-Vodyanoi Energetichesky Reaktor, water-water energetic reactor)
PHWR: Pressurized heavy water reactor
  CANDU: CANadian Deuterium Uranium reactor
Coolant  | Moderator |  |  | 
 | H2O | D2O | Graphite | None
H2O | LWR: BWR, PWR, VVER |  | LWGR: RBMK | 
D2O |  | PHWR: CANDU |  | 
Gas |  |  | Magnox AGR | 
Liquid Metal |  |  |  | LMFR

## Slide 19: Nuclear Power Reactors
LWGR: Light water graphite reactor
  RBMK: Russian Reaktory Bolshoy Moschnosti Kanalniy, high power channel-type reactor
Gas-graphite reactors
  Magnox
  AGR: Advanced Gas-cooled Reactor
FBR: Fast Breeder Reactor
Coolant  | Moderator |  |  | 
 | H2O | D2O | Graphite | None
H2O | LWR: BWR, PWR, VVER |  | LWGR: RBMK | 
D2O |  | PHWR: CANDU |  | 
Gas |  |  | Magnox AGR | 
Liquid Metal |  |  |  | LMFR

## Slide 20: Pressurized Water Reactors (PWR)
Developed in the U.S. by Westinghouse
Designed and manufactured in many countries:
  U.S.: Westinghouse and ABB/CE
  France: Framatom/Areva
  Germany: Brown Boviera
  Russia
Notes: Cochran and Tsoulfanidis, The Nuclear Fuel Cycle: Analysis and Management, p. 4.

## Slide 21: Pressurized Water Reactors (PWR)
PWRs are based on the reactor system developed for naval propulsion.
The first commercial PWR was the Shippingport Atomic Power Station outside of Pittsburgh, PA
  Designed by Westinghouse
  Operated as a standard PWR
  Operated as a light water breeder reactor (LWBR) using a thorium blanket to breed 233U
PWRs make up 66% of the U.S. commercial nuclear reactor fleet (as of 2009), and about the same percentage world-wide
Notes: Kok, Nuclear Engineering Handbook, Ch. 1

## Slide 22: Pressurized Water Reactors (PWR)
  Secondary loop prevents any reactor contamination from reaching turbine systems, allowing for simpler maintenance, replacement, and disposal.
http://www.tva.gov/power/wbndiag.htm
Uses a closed primary loop and a secondary loop that powers a steam turbine.
  Primary loop is pressurized to ~15.5 MPa to prevent boiling
  Extensive heat exchanger systems between loops
Notes: Cochran and Tsoulfanidis, The Nuclear Fuel Cycle: Analysis and Management, p. 4.

## Slide 23: Boiling Water Reactor (BWR)
The boiling water reactor was developed by Argonne National Laboratory (ANL)
They built the Experimental Boiling Water Reactor (EBWR) in Illinois:
  Initial testing at 5 MWt and 20 MWt
  Operated from 1957 to 1967 at up to 100 MWt
The first commercial BWR was the Dresden Nuclear Power Plant in Illinois
  200 MWe
  1960 to 1978
BWRs comprise 34% of the commercial nuclear portfolio in the U.S. (as of 2009)
Notes: Kok, Nuclear Engineering Handbook, Ch. 1

## Slide 24: Boiling Water Reactors (BWR)
Developed in the U.S. by General Electric
Uses a single loop:
  Light water coolant/moderator boils in the reactor vessel
  Steam dryers allow direct connection to steam turbines
http://theenergylibrary.com/node/11853

## Slide 25: Nuclear Worldwide
Kok, Ch. 1

## Slide 26: Generation IV Reactors
What makes a reactor a Generation IV reactor?

## Slide 27: Generation IV Reactors
Goals of Generation IV reactors:
  Sustainability:
    Provide near carbon-free energy
    Use fuel cycles that maximize energy efficiency and minimize waste for the good of long-term stewardship and public health
  Economics:
    Gen IV systems should have cost savings over other energy types
    The financial risk for investing in Gen IV reactors should be similar to the financial risk of other energy production methods
  Safety and reliability:
    Very low chance of core damage in emergency scenarios
    Design should remove the need for off-site emergency response
  Proliferation resistance:
    Fuel cycles must be the least attractive source of nuclear materials
    Gen IV systems should have more physical protections from terrorism than previous generations
Notes: Kok, Ch. 6