## Slide 1: Applications of Radiation

## Slide 2: Overview
General applications by radiation type
Radiography - process
Medical Research
Medical Applications
Space

## Slide 3: Alpha Radiation
Highly ionizing
Removes Static Charge
Static Charge
Alpha Particle


## Slide 4: Uses of Alpha Radiation
• Pacemakers (Older models)
• Airplanes
• Copy Machines
•Smoke Detectors
•Space exploration

## Slide 5: Beta Radiation
Small electron particle
More penetrating than alpha

e-

## Slide 6: Beta Radiation is used in thickness gauging
The thicker the material, the less radiation will pass through the material.

## Slide 7: Gauging is used to:
Measure and control thickness of paper, plastic, and aluminum.
Measure the amount of glue placed on a postage stamp
Measure the amount of air whipped into ice cream.
Measure the density of the road during construction.

## Slide 8: Back Scattering
Detector

## Slide 9: Gamma Radiation

A penetrating wave

## Slide 10: Uses for Gamma radiation
Food irradiation
Sterilization of medical equipment
Creation of different varieties of flowers
Inspect bridges, vessel welds and Statue Of Liberty.

## Slide 11: Nitrogen-14 Carbon-14 Cycle
http://science.howstuffworks.com/environmental/earth/geology/carbon-141.htm

## Slide 12: What were original uses of mysterious rays?
Becquerel’s discovery
Roentgen X-ray of Wife’s hand
Marie Curie – WWI – x-ray unit

## Slide 13: Early X-ray
Source: http://www.uihealthcare.com/depts/medmuseum/galleryexhibits/collectingfrompast/xray/xray.html

## Slide 14
Radiographs
Radiograph - radiation energy passes through object
Autoradiograph - use radiation from object itself
X-ray
Photo-Film

## Slide 15
(0.025 eV)

## Slide 16: Compare Different Materials
Cadmium ( Cd )
Lead ( Pb )
Polyethylene ( (CH3)n )

## Slide 17: CODE Box
Student Project to Demonstrate X-Ray/Neutron Radiography
Was originally in cardboard shoe box, but was replaced by more durable aluminum.

## Slide 18
C O
D E
Cadmium
Lead

## Slide 19: X-Ray Image

## Slide 20
C O
P S U
D E
Cadmium
Lead
Polyethylene

## Slide 21: Neutron Radiograph

## Slide 22: Hydrogen Fuel Cell Imaging
Fuel Cell research conducted at RSEC

## Slide 23: Hydrogen Fuel Cell Imaging
Water Calibration Wedge

## Slide 24: Hydrogen Fuel Cell Imaging

## Slide 25: Hydrogen Fuel Cell Imaging

## Slide 26: Clinical Uses of Radioactive Materials

## Slide 27: Understanding the Replication Process of the HIV Retrovirus
DNA sequencing, using 35S and 32P, is used to investigate the process by which new viruses “bud” or form from host cells

## Slide 28: 5000 Premature Infants Die Annually from Respiratory Distress/SIDS
The infant lacks a protein which produces a surfactant in the lung alveoli
Without the surfactant, there is too much surface tension – the lung is too weak to expand. A respirator is needed.
32P-research identified the missing protein
Gene therapy may one day be available

## Slide 29: Benefits from Radioisotope Research
The Penn State Artificial Heart

## Slide 30: RIA (Radio Immuno Assay)
Extremely sensitive test for the presence of radiolabeled antibodies in blood serum samples
Dr. Rosalyn Yalow developed the technique ca. 1961, won 1977 Nobel Prize
Many tests exist for:
  Adrenal Function Reproductive Hormones
  Anemia Therapeutic Drugs
  Diabetes - Related Thyroid Function
  Drugs of Abuse Tumor Markers
  Newborn Screening Veterinary Tests

## Slide 31: RIA Kit
A standard test kit includes reagents, antigens, and a minute amount of radioactivity
One kit can be used to test 100 to 500 patient serum samples

## Slide 32
14C Test for Helicobacter pylori
H. pylori is often implicated in Gastric Reflux Disease
If present, a specific antibiotic can be prescribed to eliminate it
The use of radioactive 14C provides a simple and sure test

## Slide 33: 137Cs Blood Irradiator
Delivers 2500 rads to blood products
Reduces potential for Graft-vs-Host Disease
Essential for bone marrow transplants

## Slide 34: Diagnostic Radiology Modalities
X-Ray (Roentgenology)
  Radiography
  Fluoroscopy
  CT (Computed Tomography)
  Interventional Radiology
    Angiography
    Cardiac Catheterization
    Neuro-Interventional

## Slide 35: Heart Image
Gated study of radiolabeled cardiac muscle
Allows visualization of heart tissue viability

## Slide 36: Bone Scan with 99mTc-HDP
Active bone surface is labeled
Note “hot spots” and kidneys

## Slide 37: Nuc Med & Radiographic Images Compared
Metabolic hotspots highlighted – possibly cancerous
X-ray image shows break, but no metabolic information

## Slide 38: The New(er) Kid on the Block: PET Positron Emission Tomography
18FDG Images of a normal vs an epileptic brain
Rapidly growing in popularity for tumor imaging

## Slide 39: Positron Decay and Coincidence Photon Detection
p+ à n0 + e+ + n
Positron escapes the nucleus
Two oppositely directed photons result from the annihilation of the positron with an electron
PET Scanner Coincidence Detectors

## Slide 40: 18FDG
Fluorodeoxyglucose
Most commonly used PET radiocompound
A glucose analog, useful for
  Differentiating malignant from benign tumors
  Differentiating scar from viable myocardial tissue
  Brain function studies

## Slide 41: Cerebral Glucose Metabolism
Brain tumor diagnosed
MRI scan suspicious for low-grade astrocytoma
PET/CT scan shows large hypo-metabolic are in left posterior temporal lobe
Siemens Clinical Solutions, www.medical.siemens.com

## Slide 42: Other PET Applications
Neurological studies
  Epilepsy
  Alzheimers
  Parkinson’s Disease
  Addictions
Cancer imaging and localization
  In demand by Oncologists
Cardiology studies

## Slide 43: The ‘Historical’ Problem in Modern Radiology
Images obtained from Nuclear Medicine were obtained on a computer platform different from those obtained from CT, and also from MRI, Ultrasound, etc.
Thus, images could not be easily overlaid
A common software was needed to make best use of the information from each modality

## Slide 44: Radiation Doses from Some Medical X-ray Exams
Medical Radiation (Effective Whole Body Dose Equivalent)
  Chest X-ray: 8 mrem (0.08 mSv)
  Head CT scan: 111 mrem (1.11 mSv)
  Barium Enema: 406 mrem (4.06 mSv)
  Extremity X-ray: 1 mrem (0.01 mSv)
        Source: NCRP Report 100

## Slide 45: Radiation Doses and Dose Limits
Flight from Los Angeles to London 5 mrem
Annual public dose limit 100 mrem
Annual natural background 300 mrem
Fetal dose limit 500 mrem
Barium enema 870mrem
Annual radiation worker dose limit 5,000 mrem
Heart catheterization 45,000 mrem
Life saving actions guidance (NCRP-116) 50,000 mrem
Mild acute radiation syndrome 200,000 mrem
LD50/60 for humans (bone marrow dose) 350,000 mrem
Radiation therapy (localized & fractionated) 6,000,000 mrem
Notes: 7. Radiation Doses and Dose Limits
Radioactive material has always been a natural part of the earth. It has existed for millions of years in the crust of the earth, in building materials, in the food we eat, the air we breathe, and in nearly everything that surrounds us. Radiation from these materials, as well as cosmic radiation from the sun and universe, makes up the natural background radiation to which we are constantly exposed. On the average, persons are exposed to about 300 millirem per year from natural sources.
The guidance from NCRP Report No. 116, Limitation of Exposure to Ionizing Radiation, states that for life saving or equivalent purposes, workers may approach or exceed 50,000 mrem to a large portion of the body. Emergency exposures are considered once-in-a-lifetime. This is below the threshold for the acute radiation syndrome, discussed later.
If an individual is exposed to more than 100 rem at one time, predictable signs and symptoms will develop within a few hours, days, or weeks depending on the magnitude of the dose. About half of all people exposed to a single dose of 350 rem will die within 60 days (LD50/60) without medical intervention. The large doses used in medicine for radiation therapy, while higher than this dose, are given to only part of the body and are typically given over a period of weeks.
The dose limits are highlighted in orange.

## Slide 46: MRI: Radio Waves & Magnetic Fields

## Slide 47: MRI – Magnetic Resonance Imaging
Utilizes magnetic fields and RF (radio-frequency) energy to gain information via Nuclear Magnetic Resonance
No ionizing radiation is used in this process

## Slide 48: Electricity in Space - RTG
Nuclear Options:
  Radioisotope Thermoelectric Generators (RTG)
    Work on the principle of radioactive decay.
    Energy is proportional to activity.
    Activity is proportional to half-life and amount of material.
    More material and shorter half-life means more power.
    Shorter half-life runs out sooner.
    Must balance energy supply and mission length.

## Slide 49: RTGs in Space - Theory
Works on the thermoelectric principle also known as the ‘Seebeck Effect’.
This is about 10% efficient.

## Slide 50: RTGs in Space – Half-Life
US RTGs use Pu238 as the radioactive material.
  Half-Life of 87.7 years.
  96% of energy (activity) after 5 years
  50% of energy after 87.7 years
Old US and Russian RTGs used Po210.
  Half-Life of 138 days.

## Slide 51: RTGs in Space - Radiation
Pu-238 and Po210 are alpha (α) emitters.
Alpha radiation cannot penetrate very far.
  Stopped by a sheet of paper or 10cm of air.
  Turns into heat in the RTG material.
  Very little radiation gets out of the shielding.
  Not ‘weapons grade’ material.
  Ceramic form that is very heat and impact resistant.

## Slide 52: RTGs in Space - History
1959: Atomic Energy Commission members show President
Eisenhower the new ‘nuclear battery’ for use in US satellites.

## Slide 53
Original RTG is space was for a US Navy navigation satellite.
  1961 SNAP-3 unit (Space Nuclear Auxiliary Power)
  2.7 watts of electrical power.
  Lasted for 15 years.
RTGs were used in 25 other missions from 1961 to 2005 from military satellites to the Apollo missions.
RTGs in Space - History

## Slide 54
1972: Pioneer 10 & 11 launched to explore the outer planets.
  Both survived the high radiation around Jupiter.
  Both crafts left the solar system after their mission was performed and continued to send back data for 17 years.
  Still in contact with crafts.
RTGs in Space - History

## Slide 55
1977: Voyager 1&2 launched to explore the outer planets.
  Transmitted high speed data and first high-quality pictures.
  Both crafts left the solar system after their mission was performed and continue to send back data.
RTGs in Space - History

## Slide 56
1990: Ulysses launched to explore the top and bottom of the sun.
  Mission extended after initial successes.
  First mission to explore solar system outside the ‘disk’ of the planets.
  Find the RTG.
RTGs in Space - History

## Slide 57
1989: Galileo launched to explore Jupiter and her moons.
  Took the long-way to Jupiter; by Venus and Earth twice.
  Required a long-lived power supply to make the 4-year flight.
  Operated for 14 years.
  Find the RTG.
RTGs in Space - History

## Slide 58
Galileo also needed heat for its long mission.
120 - 1watt Radioactive Heater Units (RHU) placed all over the spacecraft.
Safety design is similar to RTGs.
RTGs in Space - History

## Slide 59
1997 -Cassini Mission to Saturn and moons.
  Three General Purpose Heat Source RTGs. (current generation)
  Four-year mission once the craft gets to Saturn.
  Great results coming back from craft.
  Just discovered new moon of Saturn.
RTGs in Space - History

## Slide 60
January 2006
New Horizons Mission
  Pluto & Charon
  Kuiper Belt Objects
RTGs in Space - History

## Slide 61
Viking Landers- 1975
  Used RTGs for power
  Six Years on Nuclear Power
Mars Pathfinder-1997
  Rover used RHUs for heat.
  Three months on solar power
RTGs in Space - History